## Slide 1: Label Map Segmentation
DICOM WG-06
David Clunie
Presentation of Public Comment Draft 2024/01/08

## Slide 2: Various means of encoding segments
Previously:
  bitplanes encoding each segment (1 bit or fractional)
  allows for overlap, even if uncommon
Proposed:
  label map, in which each pixel has index into segments
  compact and efficient to process for non-overlapping use case
  very common pattern in applications that create/use segmentations

## Slide 3
1
0
0
0
0
1
0
0
0
0
1
0
0
1
0
0
Segment 1
…
1
2
3
N
0
1
2
3
N
0
1
2
0
1
2
3
0
1
0
0
0
0
1
0
0
0
0
1
0
0
1
0
Segment 2
0
0
1
0
0
0
0
1
0
0
0
0
0
0
0
1
Segment 3
0
0
0
1
0
0
0
0
1
0
0
0
0
0
0
0
Segment N
Multiple non-overlapping BINARY SEG Frames
Single LABELMAP SEG Frame

## Slide 4: Design Decisions
Re-use as much of existing Segmentation IOD as possible
New SOP Class
Documented as multiple SOP Classes, same IOD
Requirements conditioned on LABELMAP Segmentation Type
8 or 16 bit (not more)
Segment Number not required to start at and increment by 1
Color support through PALETTE COLOR Photometric Interpretation
If label maps overlap, separate instances are needed

## Slide 5: Out of Scope (for this development cycle)
More efficient description of instance rather than class segments
  e.g., thousands (millions) of nuclei
  without repeating segment sequence item describing category/property
More segments than 16 bit unsigned pixel will support
  32 bit might be needed in future for lots of instance segments
  Palette Color limited to 16 bits max at present
Improvements related to Per-Frame Functional Groups Sequence
  which gets bulky with lots of frames