## Slide 1: DICOM Educational Conference Bangkok, Thailand
OCTOBER 3-4, 2019
DICOM RESULT reporting
Structured Reports, JSON, AI
David A. Clunie
PixelMed Publishing, LLC

## Slide 2: Disclosures
Editor of the DICOM Standard (NEMA Contract)
Owner of PixelMed Publishing, LLC
Author of book on DICOM Structured Reporting
Consulting for BKMedical, Canfield, Carestream, Imago, MDDX (Bioclinica)
Supported by NIH U24CA180918 QIICR, NCI Leidos BOA 29XS219 Task Order #05

## Slide 3
Notes: http://www.freakingnews.com/A-Picture-Paints-a-Thousand-Words-Pics-65426.asp

## Slide 4
Notes: http://www.freakingnews.com/A-Picture-Paints-a-Thousand-Words-Pics-65426.asp

## Slide 5
Notes: http://www.freakingnews.com/A-Picture-Paints-a-Thousand-Words-Pics-65426.asp

## Slide 6
Notes: http://www.freakingnews.com/A-Picture-Paints-a-Thousand-Words-Pics-65426.asp

## Slide 7: What is a “Structured Report”?
Human perspective (radiologist, cardiologist, pathologist, referring physician …)
  not a massive blob of prose (narrative)
  organized
  hierarchical
  sections and sub-sections
  bulleted lists
  question and answer rather then single sentence
Machine perspective
  coded section headings
  coded questions with answers:
    coded answer
    text answer
    numeric answer (with coded units)
  links to images, regions of interest, coordinates (spatial & temporal)

## Slide 8: Machine Readable Reports

## Slide 10: Annotation – Granularity
Patient/Case
Imaging Study
Series/Acquisition
Image
Frame (pixel data array at one place in space/time/…)
Region (“of interest” – ROI)
Single point (label each/every voxel/pixel)
All supported DICOM Structured Report (SR) or SEG

## Slide 11: Annotation Representation
Contour – 2D Coordinates (SR)
Rasterized Bitmap (SEG)

## Slide 12: Presentation States relatively useless
DICOM Presentation States are great for capturing state of rendering to human
  zoom/pan, window center/width, …
  but limited text and graphic annotations
  no semantics
  not even linkage of graphics and text
  can be referenced from SR to set appropriate viewing conditions for referenced images
Unfortunately are very popular with PACS due to their simplicity
  better than no DICOM capture of annotations at all of course
  means product managers not motivated to add SR support
Ideally, all PACS viewers would support displaying any kind of SR
  not just tabulating/rendering hierarchical content as text
  not just jumping to reference image
  but also displaying all coordinates/SEG references overlaid on images
  preferably with local context from the tree such as finding, measurements and units

## Slide 13: DICOM Structured Reports
A machine-readable structured report that satisfies humans too
Added to DICOM circa 2000
Primary use-cases circa 2018
  Ultrasound cart output – echocardiography, obstetric measurements
  Mammography CAD output
  Radiation Dose from CT and projection X-Ray devices (RDSR)
  Key Object Selection (KOS)
  limited use for human-generated narrative reports with section structuring
Major new use-cases in the quantitative/machine learning era
  tumor/lesion region of interest encoding
  quantitative measurements and categorical classification
    created by humans or machines
    consumed by humans or machines

## Slide 14: DICOM Non-Image Objects
Analysis Workstation
Current DICOM Images from Modality
DICOM Segmentation
DICOM Registration
DICOM SR
DICOM Real World Value
DICOM Parametric Map Images
PACS Store, Distribute and Review
Previous DICOM Images from PACS
Previous DICOM SR etc

## Slide 15: DICOM SR organizes them …
Analysis Workstation
Current DICOM Images from Modality
DICOM Segmentation
DICOM Registration
DICOM SR
DICOM Real World Value
DICOM Parametric Map Images
PACS Store, Distribute and Review
Previous DICOM Images from PACS
Previous DICOM SR etc

## Slide 20: SR Content is a Tree
1
1
.
1
1
.2
Child Nodes
Root Node

## Slide 21: Each Node (Content Item)
Is a “name-value” pair
  e.g. “finding” = “mass”
Concept “name” is always coded
  e.g. (121071, DCM, “Finding”)
“Value” may be one of several “value types”
“Value” may be coded too
  e.g. (M-37000, SRT, “Hemorrhage”)
  e.g. 37.2 (mm2, UCUM, “square millimeters”)

## Slide 22: Value Types
TEXT
CODE
NUM
PNAME
DATE
TIME
DATETIME
CONTAINER
UIDREF
COMPOSITE
IMAGE
WAVEFORM
SCOORD(3D)
TCOORD

## Slide 23
SCCORD: Path = POLYLINE (32,77),(210,93)
NUM: Distance = 37.6 mm
INFERRED FROM
SELECTED FROM
IMAGE: 1.2.840.276453….

## Slide 24
"Individual Impression/ Recommendation"
CONTAINS
CODE: "Single Image Finding" = "Mammography breast density"
HAS PROPERTIES
SCOORD: "Outline" = POLYLINE {2531,2114,2537, 2114,..,2525,2114,2531,2114}
SELECTED FROM
IMAGE: 1.2.840.276453….
SCOORD: "Center" = POINT {2505,2168}
CONTAINER: “Mammo CAD Report”
CODE: “Summary” = “Succeeded with Findings”
CONTAINER: "Individual Impression/ Recommendation"
…

## Slide 25: Spatial Coordinates
POINT
MULTIPOINT
POLYLINE
CIRCLE
ELLIPSE

## Slide 26: Temporal Coordinates

## Slide 27: Image Temporal and Spatial Coordinates

## Slide 28: Temporal Coordinates applied to both Images and Waveforms

## Slide 29: What about Codes?
DICOM uses external lexicons
  SNOMED
  LOINC
  RADLEX
  defines DCM codes & definitions if no other good scheme
EHR push towards more reliable codes
  e.g., EHR interoperability and common data elements
  RIS, modalities and PACS implementations could do better
  institutions need to standardize internal procedure codes
  harmonize/bridge imaging/EHR codes

## Slide 30: Codes for Structured Reports
Codes needed for
  entities, e.g., lesions, tumors, tissue types
  location, e.g., anatomic site
  characteristics, e.g., edges, enhancement
  measurements, e.g., volume, sum of areas, mean
  units, e.g., HU, mm
Availability
  many already - SNOMED, LOINC, RADLEX, DCM, NCI, UCUM
  more being defined every day
  vendors also use private codes
  need to anticipate code evolution (configurable producer/consumer)

## Slide 31: ROI and Segmentation Codes

## Slide 32: ROI and Segmentation Codes

## Slide 33: Constrained by Templates
Generic tree of content items has unbounded complexity, so need constraints
Templates for interoperability for specific use cases
  e.g., Mammography CAD
Templates for entire structure
  “root level”
Templates for parts of structure – re-usable
  e.g., Volumetric ROI Measurements
Defined in PS3.16, follow pattern similar to Module tables in PS3.3
  (coded) name of content item
  requirement type
  multiplicity
  conditions
  value set for coded values
  coded units for numeric values

## Slide 35: Key Object Selection Document
Specialized form of DICOM Structured Report
  SOP Class constrains to specific template
Essentially
  list of images and other DICOM objects (“manifest”)
  coded Document Title, e.g., “For Clinical Trial Export”
  text description
Used in IHE as
  Key Image Note profile
  manifest for XDS-I profile

## Slide 36: Segmentations and Parametric Maps
Per-voxel encoding of numeric or label values
“Images”, but not just “pretty pictures”
  modality-specific or secondary capture; single or multi-frame
Segmentations
  binary, probability, fractional occupancy
  multiple segments (multiple labels)
Parametric maps
  pixel value “means something” – real world value map (RWVM)
  integers +/- (linear) rescaling to floats (usable by any viewer)
  “derived” images of modality-specific SOP Class
  recently added floating point voxels and SOP Class (Sup 172)
Leave “fusion” (superimposition) to application
  e.g., PET SUV on top of CT
  can use Blending Presentation State to specify what to fuse
Meyer P T et al. J Neurol Neurosurg Psychiatry 2003;74:471-478
Harvard Brain Atlas NRRD Label Map converted to DICOM Segmentation

## Slide 37: Traditional Binary DICOM SR

## Slide 39: Goals for Simplified DICOM SR in JSON
Full-fidelity round trip with actual DICOM SR for all constructs (any template)
Simple (enough to hand write or copy from examples)
Compact (even terse)
Understandable (relatively)
Unambiguous (easily parsable)
Leverage any existing actual or de facto JSON or evolving AI standards
Platform independent
Capable of encoding extracts separated from composite context (such as without “header” rather than content tree, image library, etc., which could be added by separate tool/pass)

## Slide 40: Pipeline to add missing stuff to JSON
Just Number, Coordinates and Image Reference
+ Lesion Identifiers
+ Image Library and Evidence Sequences
+ Composite Context
AI Algorithm
Lesion Manager
DICOM Image Aware System
Patient-Study Aware System
PACS

## Slide 41: Conclusions
DICOM has extensive result reporting encoding capability
Getting human’s to use it is challenging, beyond well established applications like ultrasound measurements
Machines can produce and consume DICOM results; e.g., mammography CAD results are always encoded as DICOM SR
Scope of ML/AI use cases for results are adequately covered
All results can be encoded as DICOM SRs, segmentations or parametric map images
Templates and codes are already defined for many applications (e.g., TID 1500 for measurements and categorical assessments)
Modern developer-friendly approaches (JSON representation of SR) are being addressed
Novel annotation mechanisms (e.g., vast numbers of nuclei in WSI) may require extensions to DICOM (à la MR tractography)