## Slide 1: Supplement 237
High resolution ECG
DICOM Working group 32
Public comment
Silvia Winkler
2022-11-18

## Slide 2: Rational
ECG data is acquired in context of neurophysiology studies
This ECG is stored using an ECG waveform object
PS3.17 Annex SSSS recommends to use General ECG Waveform object
Neurophysiology devices use other physical parameters than ECG devices
  Higher sampling frequencies: sampling frequency is not constrained for neurophysiology waveform objects
  A/D conversion using up to 32 bits per sample Waveform Sample Interpretation for neurophysiology waveform objects can be SS (signed 16 bit linear) or SL (signed 32 bit linear)

## Slide 3: Existing ECG Waveform IODs
SOP Class UID | SOP Class Name | Sampling Frequency Constraint | Waveform Sample Interpretation Constraint
1.2.840.10008.5.1.4.1.1.9.1.1 | 12-lead ECG Waveform Storage | 200 up to 1000 Hz | SS
1.2.840.10008.5.1.4.1.1.9.1.2 | General ECG Waveform Storage | 200 up to 1000 Hz | SS
1.2.840.10008.5.1.4.1.1.9.1.3 | Ambulatory ECG Waveform Storage | 50 up to 1000 Hz | SB or SS

## Slide 4: New IOD: High Resolution ECG
Shall satisfy the requirements for ECG data acquired in context of neurophysiology studies
Shall also meet requirements for ECG data
  Data acquisition with higher sampling frequencies
  A/D conversion with 32 bits per sample